## Slide 1
CompressorGuard
AI
System Architecture
Predictive Maintenance Platform for Multi-Stage Centrifugal Compressors
USERS
👤
Operations
Engineer
Browser
FRONT
END
⬡
React 18 Dashboard
• Dashboard · Training
• Evaluation · Live Monitor
• Timeline · AI Agent
◈
Real-Time UI
• SSE streaming (EventSource)
• Recharts sensor visualizations
• Tailwind dark-mode design
⇄
API Client
• Axios + 120 s timeout
• REST + Server-Sent Events
• Vite dev-server proxy
HTTP/SSE
⚡
FastAPI Backend · Python 3.11 · uvicorn · SQLAlchemy ORM
• /api/health /api/data/* /api/train/* /api/evaluate/* /api/predict/* /api/agent/* /api/predictions/*
• CORS middleware · BackgroundTasks for async training · StreamingResponse for SSE · Pydantic request validation
API
GATEWAY
ML
ENGINE
🌲
Isolation Forest
• RandomForest — 85% ensemble weight
• 50 features: 10 base + 36 temporal + 4 physics
• Rolling stats: 5/10/30 min windows
• AUC-ROC: 0.9726
∿
LSTM Autoencoder
• TensorFlow/Keras — 15% ensemble weight
• Encoder 64→32→16, Decoder 32→64→10
• 60-step sliding window input
• Reconstruction error threshold: μ + 3σ
⊕
Ensemble Predictor
• Score = 0.85×IF + 0.15×LSTM
• Threshold: Prec ≥65%, FPR ≤10%
• Confidence from model agreement
• Severity: NORMAL/LOW/MEDIUM/HIGH
🤖
Claude AI Agent
• claude-sonnet-4-6
• Structured + streaming
• Multi-turn chat
Anthropic
API
DATA
LAYER
🗄
SQLite Database (SQLAlchemy ORM)
• Prediction · AgentAnalysis · TrainingRun
• Stores: timestamps, sensor JSON, scores, severity
• CRUD helpers · auto-created on first startup
💾
Model Store (saved_models/)
• isolation_forest.pkl · if_scaler.pkl
• lstm_autoencoder.keras · lstm_meta.pkl
• optimal_threshold.json — auto-loaded at startup
📊
Data Source
• 50 000 synthetic sensor rows
• 4 fault modes: bearing, valve,
• fouling, seal leak
CompressorGuard AI · Confidential · 2025
1 / 2

## Slide 2
CompressorGuard
AI
Key Features & Capabilities
Six pillars of the CompressorGuard platform
📡
MONITORING
Live Sensor Streaming
Simulates 10 industrial sensor channels across a 3-phase fault progression — Normal, Pre-Anomaly (gradual drift), and Anomaly (critical). Displays a real-time anomaly gauge, phase banner, sensor tiles with live deviation %, and a multi-line Recharts time-series chart. All data streams via Server-Sent Events at 500 ms intervals.
10 Sensors
3 Fault Phases
500 ms Refresh
🧠
MACHINE LEARNING
Ensemble Anomaly Detection
Fuses a Random Forest classifier (85% weight, 50 features: 10 base + 36 rolling-window stats at 5/10/30 min + 4 physics-derived features) with an LSTM Autoencoder (15% weight, 60-step window). Threshold auto-tuned per evaluation to hold Precision ≥65% and false-positive rate ≤10%.
AUC-ROC 0.97+
85:15 Weighting
50 Features
🤖
AI AGENT
Claude AI Diagnosis
On each detected anomaly, invokes Anthropic claude-sonnet-4-6 via SSE token streaming. Returns a structured JSON report: root-cause hypothesis, confidence level with reasoning, affected subsystems, maintenance actions tagged Immediate / 4h / 24h / Monitor, and estimated time-to-critical. Supports full multi-turn follow-up chat.
Streaming Tokens
Structured JSON
Multi-turn Chat
⚙️
TRAINING
One-Click Model Training
Generates 50 000 synthetic sensor rows covering 4 fault modes — bearing degradation, valve issues, fouling, and seal leaks — each with a realistic 3-phase fault progression and sinusoidal load variation. Trains Isolation Forest and LSTM Autoencoder sequentially with live progress polling, then displays loss curves, thresholds, and elapsed time.
50K Rows
4 Fault Modes
Auto Threshold
📊
EVALUATION
Performance Evaluation
Full evaluation on the 20% held-out test split reporting Precision, Recall, F1, and AUC-ROC as interactive metric cards. Also renders the confusion matrix (TP/FP/FN/TN with %) an interactive ROC curve, a prediction timeline, and a lead-time histogram showing how many minutes before critical failure each anomaly was first flagged.
Prec / Recall / F1
ROC Curve
Lead-Time Histogram
🗂
HISTORY & CHAT
Anomaly Timeline & Chat
Browsable log of all predictions stored in SQLite. Filter by severity level (ALL / LOW / MEDIUM / HIGH), view an hourly aggregation bar chart, and click any event to inspect its full sensor-value breakdown. Each anomaly opens a dedicated multi-turn Claude AI chat session — conversation state persists across tab switches.
Severity Filter
Hourly Chart
Chat History
CompressorGuard AI · Confidential · 2025
2 / 2